## Slide 1
Hands-on Experience
Sensor Node

## Slide 2: IoT building blocks

## Slide 3: Some basics for IoT – we will use this
JSON
  JSON is not a protocol, but an encoding format
  Used widely in IoT
MQTT
  A lightweight messaging protocol for small sensors and mobile devices, optimized for high-latency or unreliable networks
  Client – Server - Client
  Publish – Broker – Subscribe
  Needs a Topic

## Slide 4: JSON vs XML Example
JSON Example | XML
{"employees":[ { "firstName":"John", "lastName":"Doe" }, { "firstName":"Anna", "lastName":"Smith" }, { "firstName":"Peter", "lastName":"Jones" } ]} | <employees> <employee> <firstName>John</firstName> <lastName>Doe</lastName> </employee> <employee> <firstName>Anna</firstName> <lastName>Smith</lastName> </employee> <employee> <firstName>Peter</firstName> <lastName>Jones</lastName> </employee> </employees>

## Slide 5: Sensor Node Source Code - sequence
Header Files Needed | Instantiation | MQTT & WiFi info | MQTT connection
#include "DHT.h" #include "WiFiEsp.h" #include <PubSubClient.h> #include <stdio.h> #include <stdlib.h> #include <string.h> #include <ArduinoJson.h> | DHT dht; WiFiEspClient client; PubSubClient mqttClient(client); | const char* server = "mqtt.dioty.co"; char ssid[] = “wifiSSID"; char pass[] = “wifiPasswd"; | if (mqttClient.connect(NULL, “user@name", “passwd")) { Serial.println("connected");
Read VCC | Read T&H | Format as JSON | Send to Cloud
averageVcc = averageVcc + (float) readVcc(); int16_t averageVccInt = round(averageVcc); dtostrf( averageVccInt, 3, 2, temp ); | dtostrf( dht.getHumidity(), 3, 2, temp2 ); dtostrf( dht.getTemperature(), 3, 2, temp3 ); | root["Voltage"] = temp; root["Humidity"] = temp2; root["Temperature"] = temp3; root.printTo(msg); | mqttClient.publish("/zaki.bm@gmail.com/1234", msg);

## Slide 6: MQTT
Message Queuing Telemetry Transport is an ISO standard (ISO/IEC PRF 20922)[2] publish-subscribe-based messaging protocol.
It works on top of the TCP/IP protocol.
It is designed for connections with remote locations where a "small code footprint" is required or the network bandwidth is limited.
The publish-subscribe messaging pattern requires a message broker.
FREE, open source Mosquitto MQTT. You can install on your PC
Cloud-based MQTT broker also available, example is Dioty, HiveMQ, CloudMQTT

## Slide 7: IoT Device Design – The Steps
Hardware and sensor
Make sure you can get the sensor data locally
Push the data to the cloud :
  Why?.... Because we can access it anywhere
  Where? …. Any cloud-based MQTT broker
Get the data and manipulate it :
  How?.... Use MQTT subscriber
  Manipulate?.... Yes, using tools, example is Node-Red

## Slide 8: Hardware and Sensor
Our closest friend : Handphone. This App is for Android only.

## Slide 9: Step 1: Open the App

## Slide 10: Step 2: See the dashboard

## Slide 11: Make sure you can get the sensor data locally
In the dashboard, you can see all your phone’s sensors in action
It means you are now already have the sensor data…

## Slide 12: Step 2 : See the dashboard (continue)
Toggle OFF to ON

## Slide 13: Push the data to cloud
Release the data
Let it go somewhere rather than just trapped inside your phone 
We will use MQTT service to do the work
Select any sensors you like to publish

## Slide 14: Step 3 : Stream it !
Click at “Stream”

## Slide 15: Step 3: Stream It ! (continue)
Click at MQTT stream

## Slide 16: Step 4: Fill in MQTT info
Scroll down at the same screen

## Slide 17: Step 4 : Press ON to publish the data
Data is now sent to DioTY MQTT broker

## Slide 18
See if the data goes to Cloud Server (MQTT Broker)

## Slide 19: Did MQTT broker receive the data?
By right, MQTT broker received the Data we just sent.
We can check, go to your broker to see it.

## Slide 20: The data format sent from your phone
Base Topic
Sensor-based Topic

## Slide 21: Get the data and manipulate it
Subscribe to the data
Need to use MQTT subscriber software
Once you get the data, pass it to your SW Tool.
  Show chart of the data history
  Automate action
  Send to analytics module
Example of SW Tool to do manipulation : Node-Red (open source)

## Slide 22: The Node Red Flow
Make sure you have your Node-Red running, add a New Flow
https://github.com/orenonline/LoRaWAN_WiFi_IoT_Training/
Click at “SensorNode.txt”
Click at “Raw”
Copy the whole text
Now go to your New Flow page, select Import->Clipboard
Position it nicely on the page

## Slide 23: Edit FRED node
Each items in the Node-Red is called a “node”
If you do a copy and paste, all logics are copied and pasted
But credentials are not copied and pasted.
Double-click at “MyMQTT Broker” node
Click at the small pencil
Click at the Security Tab
Fill in the Username and Password.
Click “Deploy”

## Slide 24: See the Debug and Dashboard
On the right hand side, click at the Debug tab
You can see the incoming data
For Dashboard, you can click at the Dashboard tab
All the dashboard item has been populated
All you need is just to press the small arrow underneath the Dashboard tab

## Slide 25: The Visualization

## Slide 26: Save Data into a File

## Slide 27: Config the File Node

## Slide 28: Notification to your phone
Register to Pushbullet
Install Pushbullet to your phone

## Slide 29: Install Pushbullet node

## Slide 30: Add Pushbullet to canvas
Drag in and double-click

## Slide 31: Fill up the API-key

## Slide 32: Complete the form

## Slide 33: THANK YOU
zaki.bakar@mimos.my
nordin.ramli@mimos.my
hafizal.mohamad@mimos.my
Any questions?

## Slide 34: Hardware to control AutoGate